# LYRA Instrument Manager Software requirements

## Initialisation

- The UART 1 used for data acquisition shall be initialised as follows:

- Baud rate = 38400 bauds

- Start and stop bits

- No parity

- The UART 2 used for sending telecommands to LYRA and acquiring housekeeping and status data shall be initialised as follows:

- Baud rate = TBD

- Start and stop bits

- No parity

- RAW_DATA_BUFFER (UART 1) used to store the acquired data shall have a size of TBD bytes.

- The following LYRA data management parameters shall be configurable with the following default values:

| Description | Possible value | Default value |
| --- | --- | --- |
| Science block sampling | 8 bits value | 1 |
| Rearrangement | Off – On | On |
| Compression | Off – On | On |

- At power up, the LYRA Instrument Manager shall initialise and enter the off mode.

- The number of lumps between two ASIC reload operations shall be TBD and shall be configurable.

## FDIR

- In case of latch-up (event generated by the LDM), the following shall be performed:

- Stop acquisition (LDM-TC2)

- Reload ASIC (IIU-TC4)

- Start acquisition (LDM-TC1)

- In case of buffer full (event generated by the LDM), the LIM shall switch to idle mode.

- The following monitoring shall be defined:

| Address | Content description | Monitoring |
| --- | --- | --- |
| HK 1 | Temp Filter Detector 1 | TBD |
| HK 2 | Temp Diode Detector 1 | TBD |
| HK 3 | Temp Filter Detector 2 | TBD |
| HK 4 | Temp Diode Detector 2 | TBD |
| HK 5 | Temp Filter Detector 3 | TBD |
| HK 6 | Temp Diode Detector 3 | TBD |
| HK 8 | Voltage + 9.5V | TBD |
| HK 9 | Voltage - 9.5V | TBD |
| HK 10 | Voltage + 5V | TBD |
| HK 11 | Temp VFC Print (2.5V Ref) | TBD |
| HK 12 | Temp Power Print (2.5V Ref) | TBD |
| HK 13 | Current + 28V | TBD |
| HK 14 | Current + 9.5V | TBD |
| HK 15 | Current - 9.5V | TBD |
| HK 16 | Current + 5V | TBD |
| HK 17 | Temp Heatsink | TBD |
| HK 18 | Temp Cover Plate | TBD |
| HK 19 | Temp Digital Print | TBD |
| HK 21 | Temp Reference Foot | TBD |

Action in case of monitoring limit exceeded:

- Switch to off mode

- It shall be possible to start the following contigency warm-up sequence in case the IIU has been powered off when the cover was open:

- TBD

## Functional

- It shall be possible to send TCs for immediate execution or differed execution. The standard PUS service 11 shall be used for this purpose.

- The LIM shall accept and process the following command to the LOB:

LOB-TC1: Set VFC (1/2) (ON/OFF)

LOB-TC2: Set HK group (ON/OFF)

LOB-TC3: Set detector (1/2/3) (ON/OFF)

LOB-TC4: Set cover (1/2/3) (ON/OFF)

LOB-TC5: Set cover (1/2/3) (LOCK/UNLOCK)

LOB-TC6: Set cover (1/2/3) (OPEN/CLOSE)

LOB-TC7: Set VIS LED (ON/OFF)

LOB-TC8: Set UV LED (1/2/3) (ON/OFF)

LOB-TC9: Set heater (AB/CD) on unit head (1/2/3) (ON/OFF)

LOB-TC10: Select integration time (10ms/20ms/50ms/100ms/200ms/500ms/1s/2s/5s/10s)

LOB-TC11: Select input (1/2/3/6/7/8) of multiplexer group (1/2)

LOB-TC12: Select HK address

LOB-TC13: Activate HK continuous loop

The value used to set the integration time shall be one of the following:

| Value | Integration time |
| --- | --- |
| 0 | 10 ms |
| 1 | 20 ms |
| 2 | 50 ms |
| 3 | 100 ms |
| 4 | 200 ms |
| 5 | 500 ms |
| 6 | 1 s |
| 7 | 2 s |
| 8 | 5 s |
| 9 | 10 s |
| 10 | 100 ms |
| 11 | 100 ms |
| 12 | 100 ms |
| 13 | 100 ms |
| 14 | 100 ms |
| 15 | 100 ms |

The value used to set the input of multiplexer group shall be one of the following:

| Value | Input of multiplexer group |
| --- | --- |
| 0 | Unit 1 |
| 1 | Unit 2 |
| 2 | Unit 3 |
| 3 | N/A |
| 4 | N/A |
| 5 | 5V calibration voltage (FS input) |
| 6 | 2.5V calibration voltage (HS input) |
| 7 | 0V calibration voltage (GND input) |

- It shall be possible to send the following command to the LYRA electronics:

IIU-TC1: power on/off IIU

Powering off the IIU shall be executed only if SWAP is not in use.

- It shall be possible to send the following command to the LYRA electronics:

IIU-TC2: LYRA (ON/OFF)

IIU-TC3: UV LED (ON/OFF)

IIU-TC4: Reload ASIC

- It shall be possible to configure and command the LDM:

LDM-TC1: trigger LDM for data processing.

LDM-TC2: close the current lumps.

- It shall be possible to set the LYRA Instrument Manager in one of the following modes:

- Off

- Warm-up

- Acquisition

- Idle

- The transition between modes shall be performed according to the following state diagram:

| /To From/ | Off | Warm-up | Imaging | Idle |
| --- | --- | --- | --- | --- |
| Off | N/A | TC | X | X |
| Warm-up | FDIR/TC | N/A | Auto/TC | FDIR |
| Acquisition | FDIR/TC | TC | N/A | Auto/TC |
| Idle | FDIR/TC | Auto/TC | X | N/A |

- A command to switch to Off mode shall be immediately processed, i.e. the current activity shall be cancelled.

- The syntax of the TCs shall be checked before execution and TC verification reports shall be generated

- Science raw data shall be read from RAW_DATA_BUFFER.

- LYRA housekeeping data shall be read from UART 2 every 10 seconds.

The housekeeping message shall have the format defined in ICD-CSL-LYR-04001 section 6.5

- A status message shall be read after each telecommand sent to LYRA.

The status message shall have the format defined in ICD-CSL-LYR-04001 section 6.5

- Each time an interrupt is generated, a time stamp shall be generated and saved.

LYRA transmits the gate signal every 10 seconds to the ADPMS. The low-high transition generates an interrupt at ADPMS level. Additionally the Synch Flag of the corresponding science block where the gate was sent is set

- When entering the off mode, the LIM shall perform the following:

- Close the lumps in LDM

- Prepare and send the following command word, wait TBD and verify status (3 detectors OFF, 2 VFC OFF, HK OFF, 3 covers closed)

  - Switch OFF all CD heaters of all 3 unit-heads

  - Switch OFF all AB heaters of all 3 unit-heads

  - Power HK OFF

  - Select cycling HK

  - Power all 3 Heads (assumed detectors) OFF

  - Switch OFF all VIS LEDs

  - Switch OFF all UV LEDs

  - Power ON Cover 1, 2, 3

  - Close Cover 1, 2, 3

  - Power both VFC OFF

- Prepare and send the following command word, wait TBD and verify status (3 covers closed)

  - Close Cover 1, 2, 3

- Prepare and send the following command word, wait TBD and verify status (nothing to check)

  - Power OFF Cover 1, 2, 3

- Switch OFF IIU

- When entering the idle mode, the LIM shall perform the following:

- Close the lumps in LDM

- Prepare and send the following command word, wait TBD and verify status (3 detectors OFF, 2 VFC OFF, HK ON, 3 covers closed)

  - Switch OFF all CD heaters of all 3 unit-heads

  - Switch ON all AB heaters of all 3 unit-heads

  - Power HK ON

  - Select cycling HK

  - Power all 3 Heads (assumed detectors) OFF

  - Switch OFF all VIS LEDs

  - Switch OFF all UV LEDs

  - Power ON Cover 1, 2, 3

  - Close Cover 1, 2, 3

  - Power both VFC OFF

- Prepare and send the following command word, wait TBD and verify status (3 covers closed)

  - Close Cover 1, 2, 3

- Prepare and send the following command word, wait TBD and verify status (nothing to check)

  - Power OFF Cover 1, 2, 3

- Switch OFF UV LED

- The following parameters shall be defined when entering the warm-up mode:

- LOB unit(s) 1, 2 and/or 3

- VFC(s) 1 and/or 2

- LED status ON or OFF, UV or VIS, unit 1, 2 or 3

- Cover status ON or OFF

- When entering the warm-up mode, the LIM shall perform the following:

- Close the lumps in LDM

- Switch ON LOB (Command to IIU)

- WAIT TBC 1 sec

- Prepare and send the following command word, wait TBD and verify status(3 detectors OFF, 2 VFC OFF, HK ON, 3 covers closed)

  - Switch OFF all CD heaters of all 3 unit-heads

  - Switch ON all AB heaters of all 3 unit-heads

  - Power both VFC OFF

  - Power HK ON

  - Select cycling HK

  - Power all 3 Heads OFF

  - Switch OFF all VIS LEDs

  - Switch OFF all UV LEDs

  - Power OFF Cover 1, 2, 3

  - Close Cover 1, 2, 3

- Read All HK signals (once) and verify their values TBD

- Prepare and send the following command word, wait TBD and verify status (VFC 2 ON)

  - Power VFC 2 ON

  - Select calibration channel (“Multiplexer Addr Group bits 0, 1 and 2” (val. 5, 6 or  7))

- Check channel TBD

- Prepare and send the following command word, wait TBD and verify status (VFC 1 ON, VFC 2 OFF)

  - Power VFC 2 OFF

  - Power VFC 1 ON

  - Select calibration channel (“Multiplexer Addr Group bits 0, 1 and 2” (val. 5, 6 or  7))

- Check channel TBD

- Prepare and send the following command word, wait TBD and verify status (VFC 1 OFF)

  - Power VFC 1 OFF

- Power ON LED switch in IIU (IIU_TC2)

- Prepare and send the following command word, wait TBD and verify status (detector ON, VFC ON)

  - Power desired detectors ON

  - Power desired VIS LED’s ON

  - Power desired UV LED’s ON

  - Power desired cover ON

  - Power desired VFC’s ON

- Prepare and send the following command word, wait TBD and verify status (cover open)

  - Open desired cover

- Prepare and send the following command word, wait TBD and verify status (nothing to check)

  - Power desired cover OFF

- The following parameters shall be defined when entering the acquisition mode:

- VFC calibration period (VCF_CAL_PERIOD)

- LED pulsing period (LED_PULSE_PERIOD)

- Acquisition cadence (INTEGRATION_TIME)

- When entering the acquisition mode, the LIM shall perform the following:

- Reload ASIC

- Set the acquisition cadence

- When in Off mode, the LIM shall perform the following:

- Every VCF_CAL_PERIOD seconds:

  - Application of 0V and then 2.5V and then 5V to the VFC (in loop)

- Every LED_PULSE_PERIOD seconds:

  - Switch On and then Off the LED (in loop)

## Observability

- Housekeeping data shall be made observable.

- The time stamp generated on interrupt shall be made observable.
This time stamp shall be used by the LDM.

- The commands to LYRA and their corresponding status shall be made observable.

## Performance

- The time stamp shall have an accuracy better than 5 ms w.r.t. the LYRA hardware signal.

# Text boxes

Acquisition

Warm-up

Off

Idle

FDIR/TC

FDIR/TC

FDIR

TC

TC/auto

TC/auto

TC/auto